Summary of i2c_passthru module

Basic behavior
i2c_passthru module connects two i2c channels together through an FPGA or any CMOS buffered based device.

i2c_passthru supports masters and clock stretching on either channel. While it does support master on either channel, it does not support multi master arbitration. In case of multi master arbitration and i2c_passthru begins receiving master transactions from both channels simultaneously, i2c_passthru will simply disconnect the channels and wait for both busses to be idle before reconnecting.

Design
The first channel that receives a start transaction from idle is treated as the master channel by i2c_passthru.

After this i2c_passthru keeps track of which channel should be transmitting and receiving data for any particular bit. If i2c_passthru begins receiving data on a channel at an unexpected time this is considered unexpected behavior and is detailed in the next section.

Bits are received on the expected channel, and then transmitted over to the other channel.

For example, if a master on channel A wants to read from a slave on channel B then the master on channel A will begin by transmitting a start event, followed by 7bits of address, and then a read/write bit. i2c_passthru will receive this data on channel A and begin transmiting it over onto channel B for the slave to receive. The slave is allowed to clock stretch at any point during this time, and this will cause i2c_passthru to clock stretch the master on the following bit until the slave stops clock stretching and completes the previous bit.

Following the read/write bit the slave on channel B is allowed to respond on the ack bit. During this time the master is clock stretched by i2c_passthru, and i2c_passthru sends a clock pulse to slave to receive the slave's ack bit. The slave is also allowed to clock stretch during this time, which simply delays everything.

For the 7bits of address and the read/write bit the master is transmitting every bit. During this time if the slave pulls the sda line low during any of these bits this is treated as unexpected behavior.

Similarly during the ack bit i2c passthru is receiving from the slave. If the master pulls the sda line low during this bit this is treated as unexpected behavior.

This same logic continues into the data portion of the transaction, where i2c_passthru always keeps tracks of which side should be transmitting for any bit.

Dealing with Unexpected behavior

For robustness i2c_passthru checks the bus for unexpected behavior and will disconnect and recover when needed. In this way i2c_passthru can be considered robust.

Master arbitration across the module is technically not supported, but the module has mechanisms available to disconnect the i2c bus and recover from this situation.

i2c_passthru can disconnect the bus if any of the conditions below are met:

1) scl low timeout exceeded.
If the scl or sda is stuck low on either channel beyond the timeout i2c_passthru will disconnect the bus. This parameter should be set relatively high (recommend 10ms or more).

2) slave unexpectedly controls sda or scl line.
 i2c_passthru decides which channel is the slave at the beginning of a transaction. If the slave channel controls the sda line when it isn't expected i2c_passthru will disconnect the bus. If the slave brings the scl line low from a high state then i2c_passthru will disconnect the bus. For example: if during the address phase the slave pulls the sda line low when it should be high the bus will be disconnected.

3) master unexpectedly controls sda line.
If the master channel controls the sda line when it isn't expected i2c_passthru will disconnect the bus. For example, if during a master i2c read byte the master brings the sda line low while it is expected high then the bus will be disconnected.

After a disconnect event, i2c_passthru will reconnect the bus only once both channels are idle. An i2c channel is considered idle if the scl high timeout has been exceeded, or a control stop bit has been detected on that side.